## Slide 1
3D Oil and Gas Data in
ArcGIS Pro
7/11/17
ESRI UC 2017

## Slide 2: Agenda
University Lands
Our Challenge
3D Data
ArcGIS Pro
Questions

## Slide 3: University Lands

## Slide 4: University Lands
Land set aside beginning in 1838
Appropriated Lands for University System in 1876
2.1 million acres primarily in West Texas
Revenue Supports UT & A&M Systems
Permanent University Fund (PUF) Value = $17.4 Billion
  $9.4 Billion Deposited by UL

## Slide 5: Our Challenge
Horizontal drilling introduced a new issues
  Laterals overlap in different horizons
Need to quickly identify production sources
  Land and Regulatory need to see info in 3D
ArcReader
  Can’t view 3D

## Slide 6: Our Challenge - 3D Oil & Gas Data
No GIS data was in 3D
This meant that we needed to create or acquire the 3D datasets
  Leases
  Laterals
  Perforations (first and last take points)
This data needed to be integrated with the current enterprise GIS system

## Slide 7: 3D Oil & Gas Data - Leases
Problem
Leases are stored as 2D Polygons
Leases are depth severed
Solution
Leases could be extruded based on the top and bottom depths
Multipatch feature class of leases

## Slide 8: 3D Oil & Gas Data - Laterals
Problem
Lateral information currently stored in 2D feature class
There are close to 2000 laterals on University Lands
Directional surveys are stored in Excel and PDF format
Solution
Downloaded Lateral information from third party (1200 laterals)
  Converted to GIS using ArcPy site package
Data Conversion
  corrected with UL well spots
  Added z and m value
  m value stored the measure distance
This allowed for the creation of perfs
  Tool in ArcMap but would require manual entry of each point (no batch)
  Used python script to create point along line based on measure value

## Slide 9: ArcGIS Pro - 3D Integration
Chose ArcGIS Pro
  Easy to switch between 2D and 3D maps
  Easy to integrate with current GIS architecture
  Allowed for the building of tools

## Slide 10: ArcGIS Pro - 3D Integration
Visual Nightmare
  Not useful in this form

## Slide 11: ArcGIS Pro - AOI
Area Of Interest (AOI) Tool
  Created so that a specific area could be explored
  Developed using python – What its doing

## Slide 12: ArcGIS Pro – AOI
Result after running the AOI tool
  Only Leases that intersect laterals are shown

## Slide 13: Future Plans
Recreate AOI as add-in
Include formation tops and bottoms

## Slide 14: Questions?
Scripts can be downloaded from:
  https://github.com/ULGIS/ESRIUC2017